Οδηγίες για Autocad 2002

Κατεβάζετε τα κάτωθι αρχεία:

- ‘Περιοχή Μελέτης.dwg’ (Αρχείο AutoCad)

- ‘3285.3.tif’ (χάρτης ΓΥΣ 1:5.000)

- ‘3285.3. tfw’ (γεωαναφορά χάρτη)

Τα αρχεία τα σώζετε στον υπολογιστή σας σε οποιοδήποτε φάκελο (για παράδειγμα στην επιφάνεια εργασίας).

Ανοίγετε το αρχείο AutoCad ‘Περιοχή Μελέτης.dwg’ στο οποίο δεν εμφανίζεται ο χάρτης.

Πληκτρολογείτε την εντολή image (συντομογραφία εντολής: im) η οποία ανοίγει το παράθυρο του image manager. Στο παράθυρο αυτό φαίνεται το path από όπου φορτώνετε η εικόνα η οποία συνοδεύει το σχέδιο. Το path αυτό θα πρέπει να αλλάξει και να δώσετε το path όπου πλέον έχετε αποθηκεύσει την εικόνα στον υπολογιστή σας (σύμφωνα με το ανωτέρω παράδειγμα στην επιφάνεια εργασίας). Κάνετε click πάνω στο χάρτη 3285.3 και στη συνέχεια click στο browse όπου σας δίνετε η δυνατότητα να επιλέξετε το αρχείο ‘3285.3.tif’ από το φάκελο που το σώσατε (επιφάνεια εργασίας). Τέλος κάνετε click στο ‘save path’ και OK για να κλείσετε τον image manager. Ο χάρτης πλέον πρέπει να εμφανίζεται πλέον κανονικά στο σχέδιο.

Σημείωση:

- Τα αρχεία *.tif και *.tfw πρέπει να έχουν το ίδιο όνομα και να βρίσκονται σωσμένα στον ίδιο φάκελο μαζί.

- Σε νεότερες ή διαφορετικές εκδόσεις του AutoCad (για παράδειγμα Civil 3D 2010) η εντολή για εμφάνιση του image manager είναι η ίδια (image).

ΜΕΤΑΦΡΑΣΗ:

Instructions for Autocad 2002

Download the following files:

- ‘Περιοχή Μελέτης.dwg’ (AutoCad file)

- ‘3285.3.tif’ (G.Y.S. map 1:5.000)

- ‘3285.3. tfw’ (map georeference file)

Save these files anywhere in your PC (e.g. desktop)

Open file ‘Περιοχή Μελέτης.dwg’ in which the map isn’t being displayed.

Type the command “image” (short command “im”), which opens the image manager window. In this window, you can see the path from which the drawing is loading images. This path should be changed to the path where you have saved the image in your PC (your desktop as per the above example). Click on map 3285.3 and then click “browse” which allows you to select file ‘3285.3.tif’ from its location (i.e. desktop). Finally, click “save path” and “OK” to close the image manager. The map should be displayed properly in your drawing.

Note:

- Files *.tif and *.tfw should have the same name and be stored in the same path.

- The command for bringing up the image manater (“image”) is the same for more recent or different versions of AutoCAD (e.g. Civil 3D 2010).